# Text boxes

Information
The SPAA05-NEX GPS based Antenna Alignment Tool is specially designed to improve the nominal antenna Bearing (Azimuth) of GSM, CDMA, WiMax, WiFi, DCS, Microwave and UMTS Mobile Networks.  Accurate antenna alignment can improve key performance indicators such as network accessibility and reliability.

The SPAA05-NEX system features an easy-to-use antenna mount, convenient handheld PDA, and time saving back-office software.

Main Functions
The SPAA05-NEX uses precision GPS Technology to measure, in real time; the exact antenna bearing within 2 minutes after the system is switched on.  The resulting bearing is accurate within a tolerance ± 0.5°

With conventional antenna alignment methods such as a magnetic compass or triangulation, most installation companies cannot achieve the current carrier requirement of between ± 3° and ± 5°.

For that reason most European Network operators as well as some US Network operators have made the SPAA05 tool their standard and preferred antenna alignment method.

How to use it
A simple 5-step procedure measures and stores the individual antenna bearing as well as additional site information. Our file encryption process stores the measured azimuth along with position, date, and time stamp. Back-office processing takes just a few minutes per site leaving you with a formatted report with each antenna’s azimuth.

System Accuracy
Heading: 0.5º / 0.8º / 1.5º (RMS/AVG100/Real-time)
Position: ± 1 foot
Height: ± 6.5 feet

Dimensions
HxWxD (in): 34x5x2 
Traveling HxWxD (in): 47x17x7 
Shipped Weight: 37 lbs